1.3Megapixel Water-Proof & Vandal-Proof Network Dome Camera

Features

- 1/3” 1.3Megapixel progressive scan Aptina CMOS

- H.264 & MJPEG dual-stream encoding

- Max 25/30fps@1.3M(1280×960)

- Day/Night(ICR), 3DNR, Auto iris, AWB, AGC, BLC

- Multiple network monitoring: Web viewer, CMS(DSS/PSS) & DMSS

- 3.6mm fixed lens (2.8mm,6mm optional)

- Micro SD memory, IP66, IK10, PoE

Technical Specifications

| Model | DH-IPC-HDB4100CP | DH-IPC-HDB4100CN |
| --- | --- | --- |
| Camera |
| Image Sensor | 1/3” 1.3Megapixel Aptina CMOS |
| Effective Pixels | 1280(H)x960(V) |
| Scanning System | Progressive |
| Electronic Shutter Speed | Auto/Manual 1/3~1/10000 | Auto/Manual 1/4~1/10000 |
| Min. Illumination | 0.05lux/F1.2(color) |
| S/N Ratio | More than 50db |
| Video Output | N/A |
| Camera Features |
| Max. IR LEDs Length | N/A |
| Day/Night | Auto(Electronic)/Color/B/W |
| Backlight Compensation | Off/BLC/HLC/DWDR |
| White Balance | Auto/Manual |
| Gain Control | Auto/Manual |
| Noise Reduction | 3D |
| Privacy Masking | Up to 4 areas |
| Lens |
| Focal Length | 3.6mm (2.8mm,6mm) |
| Max Aperture | F1.95 |
| Focus Control | Fixed Lens |
| Angle of View | H: 70°(97.24°/46°) |
| Lens Type | Manual/Auto Iris (DC) |
| Mount Type | Board-in Type |
| Video |
| Compression | H.264/ MJPEG |
| Resolution | 1.3M(1280×960) / 720P(1280×720) / D1(704×576) / CIF(352×288) / | 1.3M(1280×960) / 720P(1280×720) / D1(704×480) / CIF(352×240) / |
| Frame Rate | Main Stream | 1.3M/720P(1 ~ 25/30fps) |
|  | Sub Stream | D1/CIF(1 ~ 25/30fps) |
| Bit Rate | H.264: 32K ~ 8192Kbps |
| Audio |
| Compression | N/A |
| Interface | N/A |
| Network |
| Ethernet | RJ-45 (10/100Base-T) |
| Wi-Fi | N/A |
| Protocol | IPv4/IPv6, HTTP, HTTPS, SSL, TCP/IP, UDP, UPnP, ICMP, IGMP, SNMP, RTSP, RTP, SMTP, NTP, DHCP, DNS, PPPOE, DDNS, FTP, IP Filter, QoS, Bonjour, |
| ONVIF | ONVIF Profile S |
| Max. User Access | 20 users |
| Smart Phone | iPhone, iPad, Android, Windows Phone |
| Auxiliary Interface |
| Memory Slot | Micro SD, Max 32GB |
| RS485 | N/A |
| Alarm | N/A |
| PIR Sensor Range | N/A |
| General |
| Power Supply | DC12V, PoE(802.3af) |
| Power Consumption | <2.5W |
| Working Environment | -20°C~+60°C, Less than 95% RH |
| Ingress Protection | IK10 |
| Vandal Resistance | IP66 |
| Dimensions | Φ110mm×54mm |
| Weight | 0.25kg |

Dimensions (mm)

Dahua Technology Co., Ltd.

1187 BinAn Road, Binjiang District, Hangzhou, China

Tel: +86-571-87688883

Fax: +86-571-87688815

Email:overseas@dahuatech.com

www.dahuatechsecurity.com

*Design and specifications are subject to change without notice.

© 2013 Dahua Technology Co., Ltd.